## Slide 1: Ch.1: Introduction to audio signal processing
KH WONG,
CSE Dept. CUHK,
Email: khwong@cse.cuhk.edu.hk
http://www.cse.cuhk.edu.hk/~khwong

## Slide 2: References
  Audio signals processing
    Theory and Applications of Digital Speech Processing, Lawrence Rabiner , Ronald Schafer , Pearson 2011
    DAFX: Digital Audio Effects by Udo Zölzer (2nd Edition 2011) , JohnWiley & Sons, Ltd. First edition can be found at http://books.google.com.hk
    The Audio Programming Book by Richard Boulanger, Victor Lazzarini 2010, The MIT press, can be found at CUHK e-library
    Digital Audio Signal Processing by Udo Zölzer, Wiley 2008.
    Real sound synthesis for interactive applications : by Perry Cook, AK Peters
  Machine learning useful tutorials
    https://www.tensorflow.org/tutorials (GPU based)
    https://scikit-learn.org/stable/ (non-GPU based)

## Slide 3: Overview of Audio signal processing
Chapter 1: Introduction
Chapter 2: Preprocessing
Chapter 3: Feature extraction
Chapter 4: Speech compression : Vector quantization, K-means
Chapter 5: Recognition Procedures

## Slide 4: Chapter 1:
Chapter 1.A : Introduction
Chapter 1.B : Signals in time & frequency domain

## Slide 5: Chapter 1: introduction
Content
  Components of a speech recognition system
  Types of speech recognition systems
  Speech recognition Hardware
  A speech production model
  Phonetics: English and Cantonese

## Slide 6: Components of a speech recognition system
Pre-processor
Feature extraction
Training of the system
Recognition

## Slide 7: Types of speech recognition technology
Isolated speech recognition - the speaker has to speak into the system word-by-word.
Continuous speech recognition - like human.
Current products
  http://developer.android.com/reference/android/speech/SpeechRecognizer.html
  https://chrome.google.com/webstore/detail/voice-recognition/ikjmfindklfaonkodbnidahohdfbdhkn?hl=en

## Slide 8: Types depending on speakers
Speaker dependent recognition - designed for one speaker who has trained the system.
Speaker independent recognition - designed for all users without prior training.

## Slide 9: Speech recognition hardware
ADC
(analog-to-digital conversion system)
Speech
Recording
System
DAC
(Digital to Analog Converter)
Or

## Slide 10: Sampling example
16-bit
Voltage or pressure range
  0->(216-1)=65535) digitized levels
Time in ms
Sampling is at 1KHz
www.webkinesia.com/games/images/quant.gif
65535
0
Voltage
or pressure
Time in ms

## Slide 11: Conversion time and sampling time
  Human listening range (frequency) from 20Hz to 20KHz,
  Sampling frequency (freq.) must double or higher than the highest freq. (sampling theory). So, sampling for Hi-Fi music > 40KHz.
  74 minutes CD music, 44.1KHz sampling 16-bit sound=44.1KHz*2bytes*2channels*60seconds*70min.=783,216,000 bytes (747~ MB). (see http://en.wikipedia.org/wiki/CD-ROM)
  Compromise: telephone quality sound is 8KHz 8-bit sampling – still ok for human speech.

## Slide 12: A speech wave
Time samples

## Slide 13: Music wave: violin3.wav (repeated 6 times for demo purposes) (http://www.youtube.com/watch?v=xdMX5D99xgU&feature=youtu.be) Sampling Frequency=FS=44100 Hz ( 42070 samples)
How long is the play time?
Answer:(1/44100)*42070
=0.954 seconds
All 42070 samples
Zoom in to see 1000 samples
Zoom in to see 300 samples

## Slide 14: Class exercise 1.1
For a 20KHz, 16-bit sampling signal, how many bytes are used in 5 seconds?
Answer:?

## Slide 15: Sampling and reconstruction
https://edocs.uis.edu/jduva1/www/courses/455/sampling.jpg
(216-)-1= 65535
0
time
After sampling you only have the data points
You may reconstruct the signal by joining the data points

## Slide 16: Hardware for speech recognition setup
Speech is captured by a microphone , e.g.
Sampled periodically ( 16KHz) by an analogue-to-digital converter (ADC)
Each sample converted is a 16-bit data.
Tutorial: For a 16KHz/16-bit sampling signal, how many bytes are used in 1 second. (=32Kbytes)
If sampling is too slow, sampling may fail , see
http://www.ras.ucalgary.ca/grad_project_2005/asph_sampling.jpg
Sampling theorem for a signal X: The sampling frequency must be higher or equal to double the highest frequency in the signal X.
E.g.
If the highest frequency in a signal is 16K Hz, sampling frequency is 32 KHz or higher.
If the highest frequency in a signal is 20K Hz, sampling frequency is 40 KHz or higher.

## Slide 17: Exercise 1.2
If the sampling rate of the analog-to-digital conversion system is 20KHz , how large is the frequency of the sound that that can be sampled?
Answer: ________________?
If the sound is 20KHz, what is the minimum sampling rate of the analog-to-digital conversion system?
Answer: ________________?

## Slide 18: Discussion: Conversion resolution
Music
  44.1KHz , 16-bit is very good.
  Higher specifications may be used : e.g., 96 KHz sampling 24-bit
  Compression: MP3,etc can compress data
Speech
  20KHz sampling 16-bit is good enough.

## Slide 19: Class exercise 1.3
A sound is sampled at 22-KHz and resolution is 16 bit. How many bytes are needed to store the sound wave for 10 seconds?
Answer: ?
What is the highest frequency allowed in the sound signal?

## Slide 20: Signal analysis
spectrum

## Slide 21: Can we see speech?
Yes, using spectrogram.
The “time domain signal” shows the amplitude of air-pressure against time.
The “spectrogram” shows the energies of the frequency contents against time.
Time
Freq.
Spectrogram
(matlab function
spectrogram.m)
Spectrogram
time
Pressure
/output
of mic
Time domain signal

## Slide 22: Basic Phonetics
Phonemes are symbols to show how a word is pronounced.
Phonemes
Vowel
/AA/,/I/,/UH/
Diphthongs
/AY/,/AW/
Consonants
-Nasals /M/
-stops /B/,/P/
-fricative /V/,/S/
-whisper /H/
-affricates /JH/,/CH/

## Slide 23: Phonetic table
http://www.telefonica.net/web2/eseducativa/phonetics/tablea.gif

## Slide 24: Special features for Cantonese phonetics 廣東話
Each word is combined by an Initial (consonant 聲母) and a final (vowel 韵母); entering tone (入聲) are ended by /p/, /t/ or /k/
Nine tones(九聲):
  lower-flat(陽平),lower-rising(陽上),lower-go(陽去)
  higher-flat(陰平),higher-rising(陰上),higher-go (陰上)
  Entering (入聲) : ended by /p/, /t/ or /k/

## Slide 25: Summary
Studied
  Basic digital audio recording systems
  Speech recognition system applications and classifications

## Slide 26: Appendix

## Slide 27: Answer: Class exercise 1.1
For a 20KHz, 16-bit sampling signal, how many bytes are used in 5 seconds?
Answer: 20KHz*2bytes*5 seconds=200Kbytes.

## Slide 28: Answer: Exercise 1.2
If the sampling rate of the analog-to-digital conversion system is 20KHz , how large is the frequency of the sound that that can be sampled?
Answer: ___20/2=10KHz_____________?
If the sound is 20KHz, what is the minimum sampling rate of the analog-to-digital conversion system?
Answer: _______20x2=40KHz________?

## Slide 29: Answer: Class exercise 1.3
A sound is sampled at 22-KHz and resolution is 16 bit. How many bytes are needed to store the sound wave for 10 seconds?
Answer:
  One second has 22K samples , so for 10 seconds: 22K x 2bytes x 10 seconds =440K bytes
  *note: 2 bytes are used because 16-bit = 2 bytes
What is the highest frequency allowed in the sound signal?
  ANS: 11KHz because the sampling frequency is 22KHz, so the signal cannot be higher than 22KHz/2=11KHz.