## Slide 1: Ch. 4: Feature representation
Using Vector Quantization (VQ) and K-means

## Slide 2: Representing features using Vector Quantization (VQ)
Speech data is not random, human voices have limited forms.
Vector quantization is a data compression method
  raw speech 10KHz/8-bit data for a 30ms frame is 300 bytes
  10th order LPC =10 floating numbers=40 bytes
  after VQ it can be as small as one byte.
Used in tele-communication systems.
Enhance recognition systems since less data is involved.

## Slide 3: 8-bit Linear Quantization Analog–to-digital conversion
Note: 1/(2^8)=1/256= 0.00390625x1
1 Volt
0 Volt
0.00390625x1 Volts
0.00390625x2 Volts
1- 0.00390625x1 Volts
Input analog voltage Vin
0000 0000B=00 Hex
0000 0001B=01 Hex
:
:
1111 1111B=FF Hex
1111 1110B=FE Hex
1- 0.00390625x2 Volts
34H,38H,76H ….
E.g.
E.g.
Quantized 8-bit value representation
if Vin falls into this range

## Slide 4: Use of Vector quantization for Further compression
If the order of LPC is 10, it is a data in a 10-dimensional space
after VQ it can be as small as one byte.
Example, the order of LPC is 2 (2 D space, it is simplified for illustrating the idea)
e:
i:
u:
LPC coefficient a1
LPC coefficient a2
e.g. same voices (i:) spoken by the same person at different times

## Slide 5: Vector Quantization (VQ) (weeek3) A simple example, 2nd order LPC, LPC2
We can classify speech sound segments by Vector quantization
Make a table
 | Sound | Mean values of samples | 
code |  | Lpc code: a1 | Lpc code:a2
1 | e: | 0.5 | 1.5
2 | i: | 2 | 1.3
3 | u: | 0.7 | 0.8
Feature space and sounds are
classified into three different types
e:, i: , u:
e:
i:
u:
The standard sound is
the centroid of all
samples of e: (a1,a2)=(0.5,1.5)
The standard sound is
the centroid of all
samples of I (a1,a2)=(2,1.3)
The standard sound is the centroid of all samples of u:, (a1,a2)=(0.7,0.8)
a2
a1
1
2
2
Using this table, 2 bits are
enough to encode each sound

## Slide 6: Another example LPC8
256 different sounds encoded by the table (one segment which has 512 samples is represented by one byte)
Use many samples to find the centroid of that sound, “i”,“e:”, or “i:”
Each row is the centroid of that sound in LPC8.
In telecomm sys., the transmitter only transmits the code (1 segment using 1 byte), the receiver reconstructs the sound using that code and the table. The table is only transmitted once at the beginning.
Code (1 byte) | a1 | a2 | a3 | a4 | a5 | a6 | a7 | a8
0=(e:) | 1.2 | 8.4 | 3.3 | 0.2 | .. | .. | .. | ..
1=(i:) | .. | .. | .. | .. | .. | .. | .. | ..
2=(u:) |  |  |  |  |  |  |  | 
: |  |  |  |  |  |  |  | 
255 | .. | .. | .. | .. | .. | .. | .. | ..
transmitter
receiver
One segment (512 samples ) compressed into 1 byte

## Slide 7: VQ techniques, M code-book vectors from L training vectors
Method 1: standard K-means clustering algorithm(slower, more accurate)
  Arbitrarily choose M vectors
  Nearest Neighbor search
  Centroid update and reassignment, back to above statement until error is minimum.
Method 2: Binary split K-means (faster) clustering algorithm, this method is more efficient.
Video Demo:
https://www.youtube.com/watch?v=BVFG7fd1H30
Matlab Demo
  http://www.mathworks.com/matlabcentral/fileexchange/16762-k-means-algorithm-demo

## Slide 8: Method 1: Standard K-means
Example: the goal is to partition these sample data into 3 clusters (groups).

## Slide 9
The Standard K-means algorithm

## Slide 10: Method 1: Standard K-means example for 3 clusters
Step1: Randomly select 3 samples among the candidates as centroids. Each centroid represents a cluster (a group) .
Step2: For each sample, find the nearest centroid and that sample becomes a member of that cluster.
After step2, three
clusters are formed
= randomly selected
as centroid at the beginning

## Slide 11: Method 1: Standard K-means
Step3: Find the new centroid within a cluster for all clusters.
Step4: Regroup all samples based on the new centroids.
Step5: Repeat until no change of grouping. Each final centroid is the presentative of that cluster. Done!
=New centroid
=Old centroid

## Slide 12: Method 2(more efficient):Binary split K-means:(assume you use all available samples in building the centroids at all stages of calculations)
Split function:
new_centroid=
old_centriod(1+/-e),
for 0.01e  0.05
A simplified model of the Binary split K-means VQ algorithm
m is the counter of how many clusters are current using.
M is the number of clusters you want
1 centroid
2 centroids
4 centroids
8 centroids
splitting

## Slide 13: Example: VQ : 240 samples use VQ-binary-split to split to 4 classes
Steps
Step1: all data find centroid C
C1=C(1+e)
C2=C(1-e)
Step2:
Split the centroid into two C1,C2
Regroup data into two classes according to the two new centroids C1,C2

## Slide 14: continue
Stage3:
Update the 2 centroids according to the two spitted groups
Each group find a new centroid.
Stage 4: split the 2 centroids again to become 4 centroids

## Slide 15: Final result
Stage 5: regroup and update the 4 new centroids, done.
Video Demo: 3D , 3 clusters
demo041_kmeans_demo_3D video

## Slide 16: Exercise 4.1: VQ
Given 4 speech frames, each is described by a 2-D vector (x,y) as below.
P1=(1.2,8.8); P2=(1.8,6.9); P3=(7.2,1.5); P4=(9.1,0.3).
  Use K-means method to find the two centroids.
  Use Binary split K-means method to find the two centroids. Assume you use all available samples in building the centroids at all stages of calculations
  A raw speech signal is sampled at 10KHz/8-bit. Estimate compression ratio (=raw data storage/compressed data storage) if LPC-order is 10 and frame size is 25ms with no overlapping samples.

## Slide 17: Exercise 4.2: Binary split K-means method for the number of required centroids is fixed (assume you use all available samples in building the centroids at all stages of calculations) .Find the 4 centroids
P1=(1.2,8.8);P2=(1.8,6.9);P3=(7.2,1.5);P4=(9.1,0.3),P5=(8.5,6.0),P6=(9.3,6.9)
first centroid C1=((1.2+1.8+7.2+9.1+8.5+9.3)/6, 8.8+6.9+1.5+0.3+6.0+6.9)/6) = (6.183,5.067)
Use e=0.02 find the two new centroids
Step1: CCa= C1(1+e)=(6.183x1.02, 5.067x1.02)=(6.3067,5.1683)
CCb= C1(1-e)=(6.183x0.98,5.067x0.98)=(6.0593,4.9657) CCa=(6.3067,5.1683) ; CCb=(6.0593,4.9657)
The function dist(Pi,CCx )=Euclidean distance between Pi and CCx
Points | Dist. To CCa | -1 *Dist. To CCb | Diff | Group to
P1 | 6.2664 | -6.1899 | 0.0765 | CCb
P2 | 4.8280 | -4.6779 | 0.1500 | CCb
P3 | 3.7755 | -3.6486 | 0.1269 | CCb
P4 | 5.6127 | -5.5691 | 0.0437 | CCb
P5 | 2.3457 | -2.6508 | -0.3051 | Cca
P6 | 3.4581 | -3.7741 | -0.3160 | CCa
Group to the side
(a or b) if |diff| for that side is smaller

## Slide 18: Recall: Application of K-means to build the vector quantization (VQ) table
Record many sound samples, each sound sample should belong to one of the 256 clusters (sound group) such as a “i”,“e:”, “i:”.. etc. Construct the VQ table as follows.
Use K-means to find 256 centroids , each is an representation of that sound group.
Each row is a centroid which has 8-columns, each column is an LPC code (a1,..,a8 etc.)
Use one byte to index each row, enough for a table of 256 rows.
In telecomm sys., the transmitter only transmits the code (1 sound segment of 20ms using 1 byte), the receiver reconstructs the sound using that code and the table. The table is only transmitted once at the beginning. This table can also be used for speech recognition.
Code (1 byte) | a1 | a2 | a3 | a4 | a5 | a6 | a7 | a8
0=(e:) | 1.2 | 8.4 | 3.3 | 0.2 | .. | .. | .. | ..
1=(i:) | .. | .. | .. | .. | .. | .. | .. | ..
2=(u:) |  |  |  |  |  |  |  | 
: |  |  |  |  |  |  |  | 
255 | .. | .. | .. | .. | .. | .. | .. | ..
transmitter
receiver
One segment (512 samples ) compressed into 1 byte

## Slide 19: 4.3 Exercise
X =[1.5 5.9
0.6 4.2
4.9 8.5
9.5 10
7.0 9.5
6.9 0.3
11.2 4.2
4.8 2.1]
e=0.1
Use Binary Split K-means to find centroids of 4 cluster 4
Answer:
% Answer:
%matlab code
X =[1.5 5.9
0.6 4.2
4.9 8.5
9.5 10
7.0 9.5
6.9 0.3
11.2 4.2
4.8 2.1]
[cts,c]=kmeans(X,4)
cts
c
%run the above to check the result
%warning https://www.mathworks.com/matlabcentral/answers/367432-k-means-clustering-giving-different-results
%K-means clustering giving different results
%So, the results depend on the initial guess which is random. But if you have large number of sample data, the result is more stable and acceptable.

## Slide 20: Summary
Learned
  Audio feature types
  How to extract audio features
  How to represent these features

## Slide 21: Appendix

## Slide 22: Answer 4.1 : Class exercise 4.1 : K-means method to find the two centroids
P1=(1.2,8.8);P2=(1.8,6.9);P3=(7.2,1.5);P4=(9.1,0.3)
Arbitrarily choose P1 and P4 as the 2 centroids. So C1=(1.2,8.8); C2=(9.1,0.3).
Nearest neighbor search; find closest centroid
  P1-->C1 ; P2-->C1 ; P3-->C2 ; P4-->C2
Update centroids
  C’1=Mean(P1,P2)=(1.5,7.85); C’2=Mean(P3,P4)=(8.15,0.9).
Nearest neighbor search again. No further changes, so VQ vectors =(1.5,7.85) and (8.15,0.9)
Draw the diagrams to show the steps.

## Slide 23: Answer for exercise 4.1
  A raw speech signal is sampled at 10KHz/8-bit. Estimate compression ratio (=raw data storage/compressed data storage) if LPC-order is 10 and frame size is 25ms with no overlapping samples.
Answer:
Raw data for a frame is 25ms/(1/10KHz)=25*10^-3/(1/(10*10^3)) bytes=250 bytes
LPC order is 10, assume each code is a floating point of 4 bytes, so totally 40 bytes
Compression ratio is 250/40=6.25

## Slide 24: Answer 4.2: Binary split K-means method for the number of required contriods is fixed (assume you use all available samples in building the centroids at all stages of calculations)
P1=(1.2,8.8);P2=(1.8,6.9);P3=(7.2,1.5);P4=(9.1,0.3)
first centroid C1=((1.2+1.8+7.2+9.1)/4, 8.8+6.9+1.5+0.3)/4) = (4.825,4.375)
Use e=0.02 find the two new centroids
Step1: CCa= C1(1+e)=(4.825x1.02,4.375x1.02)=(4.9215,4.4625)
CCb= C1(1-e)=(4.825x0.98,4.375x0.98)=(4.7285,4.2875) CCa=(4.9215,4.4625)
CCb=(4.7285,4.2875)
The function dist(Pi,CCx )=Euclidean distance between Pi and CCx
points dist to CCa -1*dist to CCb =diff Group to
P1 5.7152 -5.7283 = -0.0131 CCa
P2 3.9605 -3.9244 = 0.036 CCb
P3 3.7374 -3.7254 = 0.012 CCb
P4 5.8980 -5.9169 = -0.019 CCa

## Slide 25
Answer 4.2: Nearest neighbor search to form two groups. Find the centroid for each group using K-means method. Then split again and find new 2 centroids. P1,P4 -> CCa group; P2,P3 -> CCb group
Step2: CCCa=mean(P1,P4),CCCb =mean(P3,P2);
CCCa=(5.15,4.55)
CCCb=(4.50,4.20)
Run K-means again based on two centroids CCCa,CCCb for the whole pool -- P1,P2,P3,P4.
points dist to CCCa -dist to CCCb=diff2 Group to
P1 5.8022 -5.6613 = 0.1409 CCCb
P2 4.0921 -3.8148 = 0.2737 CCCb
P3 3.6749 -3.8184 = -0.1435 CCCa
P4 5.8022 -6.0308 = -0.2286 CCCa
Regrouping we get the final result
CCCCa =(P3+P4)/2=(8.15, 0.9); CCCCb =(P1+P2)/2=(1.5,7.85)

## Slide 26
P1=(1.2,8.8);
P2=(1.8,6.9)
P3=(7.2,1.5);
P4=(9.1,0.3)
C1=(4.825,4.375)
CCb= C1(1-e)=(4.7285,4.2875)
CCa= C1(1+e)=(4.9215,4.4625)
Step1:
Binary split K-means method
for the number of required
contriods is fixed, say 2, here.
CCa,CCb= formed
Answer 4.2

## Slide 27
CCCa=(5.15,4.55)
CCCb =(8.15,0.9)
P1=(1.2,8.8);
P2=(1.8,6.9)
P3=(7.2,1.5);
P4=(9.1,0.3)
Step2:
Binary split K-means method
for the number of required
contriods is fixed, say 2, here.
CCCa,CCCb= formed
CCCb=(4.50,4.20)
Direction
of the split
CCCCb=(1.5,7.85)
CCCCa=(8.15,0.9)
Answer 4.2

## Slide 28: 4.3 Exercise
X =[1.5 5.9
0.6 4.2
4.9 8.5
9.5 10
7.0 9.5
6.9 0.3
11.2 4.2
4.8 2.1]
e=0.01
Use Binary Split K-means to find centroids of 4 clusters.
Answer: